## Slide 1: 3D Printing Research
Fit tolerances
length of screws
Private contractors

## Slide 2: Different Types of Fits
RC – Running/Sliding Fits
  Meant for parts in motion
Locational Fits
  LC – Clearance Locational Fits
    Meant for parts that are normally stationary, but can be easily assembled or disassembled
  LT – Transitional Locational Fits
    Meant for parts that allow a small amount of clearance or interference
  LN – Interference Locational Fits
    Meant for parts that require accurate locations and rigidity
FN – Force/Shrink Fits
  Mean for parts designed to transmit frictional loads from one part to another by the tightness of fit

## Slide 3: Venturi Tube & Box
Since this is a part that is meant for easy assembly and disassembly, we should use a clearance locational fit
Low range with tight clearance (LC 1-2)
High range with large clearance (LC 10-11)
H7/h6 preferred for our needs
  Correlates to LC 2
Use calculator (or table)
  https://www.engineersedge.com/calculators/mechanical-tolerances/ansi-fit-tolerances.htm

## Slide 4: Required Tolerance (0.904" nom)
HOLE (Venturi Tube)
  Max - 0.9048”
  Min - 0.904”
SHAFT (Box)
  Max - 0.904”
  Min - 0.9035”
Total max clearance: 0.0013”
Total min clearance: 0

## Slide 5: Printed Venturi Tube
Tab is 0.9045"
Old pressure transducers stick out 1.25"

## Slide 6: 3D Printing Tolerance
Ultimaker 2+
  We’ve experienced an excess of material for our o-ring test part
  Try to slow down the print for higher accuracy
Outsourced 3D printer for venturi
  Assume it’s essentially perfect compared to Ultimaker
Choose the fit with the largest hole tolerance and lowest shaft tolerance
  Shaft: 0.9035” (tab)
  Hole: 0.9048” (box)
Diameter of the box: 0.9048”
Diameter of the tab: 0.9035”
Notes: Clearance = 0.0013"
Printed box = 0.9045"
New box dimension = 0.9058"

## Slide 7: Screw Length
Using 4-40 screws
  0.112” nominal diameter
  40 threads per inch
Thickness of box top is 0.125”
General Rules
  The length of the thread in the component connected should be at least twice the diameter of the fastener (> 0.224”) [Inserts are 0.135"]
  Total length of the screw must be at least 0.125” + 0.224” = .35”
  Free-fit clearance hole drills should be 0.1285” (size 30) according to the Engineers Handbook (see link in notes)
Length of screw >= 0.35”
Clearance hole in top: 0.1285”
Ours is 0.3125"
Notes: https://cdn.groupbuilder.com/biplaneforum/uploads/20080913_055308_taphole.pdf

## Slide 8: Private Companies – Venturi Tube Only (Contacted)
Previous material: Ultem (Which grade?)
https://triton3d.com/print-service/ Ultem 1010 PEI
  Rush order (2 days): $200 + $8 delivery (see notes)
  Bulk of cost is from startup fee – additional quantity is less than $1
https://www.aetnaplastics.com/forms/request-for-quote
  Quote pending
stratasysdirect.com
  $147 – additional quantities just as expensive
  3 days to fabricate before shipping
Notes: https://digifabster.com/client/invoice/41976/278924bfbaec1fda6a3d9da8988e0e7c05ce981d4901f505da889138/pdf/?budget_offer=1

## Slide 9
https://visionminer.com/pages/3d-print-service-manager
  $571.66 (Auto Quote)
Bert’s 3D Printing Service
  $107.77
https://www.intamsys.com/printingservice/
  Quote Pending
3 Space
  Minimum order $250 for Ultem 9085 (3 Venturi Tubes)

## Slide 10: Company Responses
INTAMSYS – No go
3 Space
  $250 for order of 3
3DXTECH
  1 week $336.77
  2 day $596.77
StratasysDirect
  $124 (each for order of 10)
Vision Miner
  $650